ELF Network Data

Tohoku University

March 21, 2006

[Notice of Data Usage]

- All of the ELF Network cataloged in this database are open to use for scientifeic studies freely.

- When the ELF data will be presented at any scientific meetings or publications, please acknowledge as ”The ELF data of sprites are provided by Tohoku University”.

- For more detail information about the ELF data, please contact following respondents.

Prof. Hiroshi Fukunishi　　 fuku@pat.geophys.tohoku.ac.jp

Prof. Yukihiro Takahashi　 yukihiro@pat.geophys.tohoku.ac.jp

tel) +81-22-217-6734 or 5775   fax) +81-22-217-5775

[Data Format]

- It is observed by a search coil magnetometer and is recording with PC.

The components of north-south and east-west are always observed at world 3 points:

South Antarctica-Showa base (39.5 degree E, 69.0 degree S), Miyagi     Prefecture-Onagawa Observatories (141.5degreeE, 35.4degreeN), and Sweden -Esrange (21.1degreeE, 67.9degreeN).

- Observations frequency is 1-100 Hz, and a sampling frequency is 400Hz.

- One file is made for every minute and it has become 1440 files in one day.

- It is about 500MB per day in amount of data in about 300-400KB per file.

[Data Catalog]

- What asked for the dynamic spectrum in January of the data acquired in 2005 using every day in February and the data taken about every three days in May - October on the Showa base was recorded.

- FFT conversion of the file in every minute was carried out, respectively, the frequency at vertical axis, time at horizontal axis and it plotted daily.

- Because the periodical error by the data deficit or PC is using another file instead, the unnatural pattern has come out of it in some places.

- The data of three points in February 1, 2005 00:00:00UT - 00:05:00UT was recorded as sample data.

- Reading of a file name「EM1_050201_000300.dat」

  - They are shown that EM1 is data of Showa, EM2 is data of Onagawa, EM3 is data of Esrange.

  - 050201　―＞　February 1, 2005

  - 000300　―＞　00:03:00UT

- A file is DAT form and can be read by a common

editor.

- The view of a file

  - The 1st line is header.

  - The 2nd line or subsequent ones is data,

    - The 1st row is an IRIG-E code.

    - The 2nd row is a north-south component.

    - The 3rd row is an east-and-west component.

  - For changing to magnetic field data, a data value is multiplied by [x10/32768/0.3/amp-gain].

―＞［nT］

  - amp-gain is Showa [x320], Onagawa [x80], and Esrange [x100].

[Data Catalog in Tohoku University]

It describes only about henceforth in 2005. Moreover, it describes only about data deficits because it is always observed fundamentally.

Showa Data

Month	Deficit day

05-01	23,24

05-02

05-03	30,31

05-04	01～06

05-05	11,12,18

05-06

05-07

05-08	9

05-09

05-10

05-11

05-12

Onagawa Data

Month	Deficit day

05-01	13

05-02

05-03

05-04

05-05

05-06

05-07

05-08

05-09

05-10

05-11

05-12

Esrange Data

Month	Deficit day

05-01

05-02

05-03	14,15

05-04

05-05	4-10,28

05-06

05-07

05-08	18

05-09

05-10

05-11

05-12

# Text boxes

1.	2005,2,1,0,3,0,400,3,"SYO"

2.	3229,-506,21

3.	3228,-578,-501

4.	3226,-573,-1079

5.	3230,-467,-1304

//////////////////////////

23999.	-9,-189,-117

24000.	-8,-123,8

24001.	-7,2,11